## Slide 1: Expanding Disk Extended Color BASIC
Brendan Donahe
Notes: Introduce myself…
While this is a presentation about how I added more commands to DECB (that is, Disk Extended Color BASIC for the CoCo 1 and 2) for CoCoVGA. Despite the functional ties to CoCoVGA, I’ll try to make the vast majority of this more general-purpose and an example of what you could do.

## Slide 2: Why Expand BASIC Further? The case for BASIC
Accessibility/Ubiquity - BASIC is in ROM on all CoCos and has straightforward syntax similar to other systems of the era
Numerous CoCo BASIC hobbyists: Long-standing request from users for easier way to access CoCoVGA enhanced features through BASIC without lots of pokes and loading of ML routines
CoCo Microsoft BASIC lends itself to extension!
Notes: Why BASIC? Why do we care about BASIC?
In ROM on all CoCos – turn it on and it’s the first thing you see (assuming you don’t have a game cartridge installed).
Easy syntax for hobbyists and novices to get used to.
It’s a much more common request among CoCoVGA users to support BASIC than anything else.
Last, but not least, Microsoft BASIC on the CoCo lends itself to extension!

## Slide 3: CoCo 1/2 DECB Memory Map
Region | Size | Contents
$0000-$03FF | 1024 | BASIC system RAM (incl. hooks and jump table ptrs!)
$0400-$05FF | 512 | 32-column text and semigraphics
$0600-$0DFF | 512 | Disk system RAM
$0E00-$7FFF | 29184 | Graphics memory, user’s BASIC program, stack space
$8000-$9FFF | 8192 | Extended Color BASIC ROM
$A000-$BFFF | 8192 | Color BASIC ROM
$C000-$DFFF | 8192 | Disk BASIC ROM (usage varies by controller/cartridge)
$E000-$FEFF | 7935 | Unused
$FF00-$FFFF | 256 | I/O control registers, vector table
http://www.cocopedia.com/wiki/index.php/Color_Computer_2_Memory_Map
Notes: Let’s start by talking about the 64k (well, and 32k) DECB (Disk Extended Color BASIC) CoCo 1 and 2 memory map.
The lower 32k (with lighter color background) is a RAM region for BASIC and user usage.
The upper 32k is mostly ROM and control registers.
Note that there are some RAM hooks and jump tables we can modify because Microsoft put them in low RAM!

## Slide 4: Builtin DECB Extensibility Features
0322 ** THE LAST USED TABLE MUST BE FOLLOWED BY A ZERO BYTE 0323 * THE JUMP TABLE VECTORS (3,4 AND 8,9) POINT TO THE JUMP TABLE FOR 0324 * THE FIRST TABLE. FOR ALL OTHER TABLES, THESE VECTORS POINT TO A 0325 * ROUTINE WHICH WILL VECTOR YOU TO THE CORRECT JUMP TABLE. 0329 0330 * BYTE DESCRIPTION 0331 * 0 NUMBER OF RESERVED WORDS 0332 * 1,2 LOOKUP TABLE OF RESERVED WORDS 16-bit addr 0333 * 3,4 JUMP TABLE FOR COMMANDS (FIRST TABLE) (CB ONLY) 0334 * VECTOR TO EXPANSION COMMAND HANDLERS (ALL BUT FIRST TABLE) 16-bit addr 0335 * 5 NUMBER OF SECONDARY FUNCTIONS 0336 * 6,7 LOOKUP TABLE OF SECONDARY FUNCTIONS (FIRST TABLE) 0337 * VECTOR TO EXPANSION SECONDARY COMMAND HANDLERS (ALL BUT 0338 * FIRST TABLE) 0339 * 8,9 JUMP TABLE FOR SECONDARY FUNCTIONS 0341 0342 0120 COMVEC RMB 10 BASIC'S TABLE token number starts at $80 + 53 = $B5 0343 012A RMB 10 EX BASIC'S TABLE token number + 25 = $CE 0344 0134 RMB 10 DISC BASIC'S TABLE token number + 19 = $E1 0345 0362 013E RMB 10 USER (SPARE) COMMAND INTERPRETATION TABLE SPACE 0363 0148 FCB 0 END OF COMM INTERP TABLE FLAG
(Taken and heavily edited from the Color/Extended/Disk BASIC Unravelled II books)
Notes: This is a heavily edited excerpt from the BASIC Unravelled book series. Note that this describes 4 pairs of tables, one each for:
Color BASIC with 10 bytes at hex 120
Extended Color BASIC with 10 bytes at hex 12A
Disk BASIC with 10 bytes at hex 134
User space with 10 bytes at hex 13E
I have also taken the liberty of striking out the 2nd table in each pair in the description above. The 1st table is for commands, the 2nd (unneeded) table in this context is for BASIC functions (which return data)
Walk through...

## Slide 5: Why Two Tables?
BASIC tokenizer uses first table to convert BASIC command and function strings to single-byte token numbers in RAM
  Saves memory
  Reduces runtime – string compares for commands no longer needed
During program execution, BASIC able to use token as an index through the second (jump) table to execute appropriate routine
Notes: Why are there both a lookup table of reserved words and an interpreter jump table?
The first is for the tokenizer – BASIC converts commands and function strings into single-byte numbers in memory – the TOKEN
The second is for during program execution – the token values can be used as indices through a jump table to the function of interest

## Slide 6: CoCoVGA BASIC Extension 0.2 Commands
VRESET
VPALETTE slot, red, green, blue, now
VFONT font, lowercase, inversevideo
VARTIFACT coloron, swap, mode
VBORDER mode, quiet
VLOADCHARS [address]
VSCANLINES on
VWIDTH width
Notes: Here are the 8 commands I have added. Don’t worry, we won’t go through the code for all of them, but I will describe some of the setup for some of them and how we deal with numeric byte-sized arguments

## Slide 7: Table Construction
String table (“LOOKUP TABLE OF RESERVED WORDS”)
comtbl
FCS "VRESET"
FCS "VPALETTE"
FCS "VFONT"
FCS "VARTIFACT"
FCS "VBORDER"
FCS "VLOADCHARS"
FCS "VSCANLINES"
FCS "VWIDTH"
Jump table (“JUMP TABLE FOR COMMANDS”)
jumptbl
FDB vreset
FDB vpalette
FDB vfont
FDB vartifact
FDB vborder
FDB vloadchars
FDB vscanlines
FDB vwidth
Notes: On the left we have the string table used by the tokenizer to convert what the user typed into a token value.
On the right is the jump table with 16-bit entry point addresses to functions I’ve written
Note the one-to-one mapping between these tables

## Slide 8: Tokenized Instruction Dispatch
* Number of commands
numcmd EQU 8
* Biggest token number from DECB
hitoken EQU 0xE1
comcod
CMPA #hitoken+numcmd
BLS goodcmd
synerr
JMP $B277 ; Unrecognized token - jump into BASIC
; syntax error routine
goodcmd
LDX #jumptbl
SUBA #hitoken+1
JMP $ADD4 ; Jump back into BASIC with index into
; jump table

## Slide 9: C Loader
#define CCVB_NUMCMD 8 // Number of new commands "numcmd"
#define CCVB_COMTBL 0xEE00 // Lookup table of reserved words "comtbl"
#define CCVB_INTERP 0xEE86 // Command interpreter "comcod"
#define CCV_BASIC_TABLE_START 0x13e
unsigned char *ccv_basic_table_hook =
(unsigned char *)CCV_BASIC_TABLE_START;
ccv_basic_table_hook[ 0] = (unsigned char)(CCVB_NUMCMD);
ccv_basic_table_hook[ 1] = (unsigned char)(CCVB_COMTBL >> 8);
ccv_basic_table_hook[ 2] = (unsigned char)(CCVB_COMTBL & 0xFF);
ccv_basic_table_hook[ 3] = (unsigned char)(CCVB_INTERP >> 8);
ccv_basic_table_hook[ 4] = (unsigned char)(CCVB_INTERP & 0xFF);
ccv_basic_table_hook[ 5] = (unsigned char)0; // No functions
ccv_basic_table_hook[10] = (unsigned char)0; // No more tablesiu
Notes: Here, the C loader code is placing 16-bit pointers to these tables in bytes 1 and 2 and 3 and 4. It also provides the number of commands in these tables in byte 0.

## Slide 10: 64k CoCo 1/2 DECB Memory Map
Region | Size | Contents
$0000-$03FF | 1024 | BASIC system RAM
$0400-$05FF | 512 | 32-column text and semigraphics
$0600-$0DFF | 512 | Disk system RAM
$0E00-$7FFF | 29184 | Graphics memory, user’s BASIC program, stack space
$8000-$9FFF | 8192 | Extended Color BASIC ROM
$A000-$BFFF | 8192 | Color BASIC ROM
$C000-$DFFF | 8192 | Disk BASIC ROM (usage varies by controller/cartridge)
$E000-$FEFF | 7935 | Unused – good place for more code/data!
$FF00-$FFFF | 256 | I/O control registers, vector table
http://www.cocopedia.com/wiki/index.php/Color_Computer_2_Memory_Map
Could use CLEAR to reserve memory between $E00 and $7FFF, but since I have 64k, would prefer to use $E000 to $FEFF since stock BASIC can’t use it anyway
Notes: You may have caught this already in the last slide – addresses in high memory for our tables and command interpreter...Returning to our memory map notice that I’ve turned the boring grey unused region to a nice bright green! We want to use this as much as possible and avoid using the lower 32k that the user needs and stock BASIC uses – but how do we get to it?

## Slide 11: CoCo 1/2 with 64k RAM
6883 SAM (Synchronous Address Multiplexer) enables remapping upper memory from ROM to RAM using TY control register
Any store to $FFDE sets memory map to 32k RAM lower/32k ROM upper (default at boot)
Any store to $FFDF sets memory map to 64k RAM, revealing upper “hidden” 32k RAM previously obscured by ROM
Notes: Here comes the SAM to the rescue! On a 64k CoCo 1 or 2, we can use it to remap that upper 32k from ROM into RAM.
Refer to slide...

## Slide 12: Copy ROM to RAM
; Taken from Allen Huffman’s
; https://subethasoftware.com/2016/01/19/64k-trs-80-coco-memory-test/
ORCC #$50 ; Disable interrupts
LDY #$8000 ; Start copy at 0x8000
copy6:
STA $FFDE ; Make ROM appear at 0x8000+
LDD ,Y ; Read
LDX 2,Y ; 6
LDU 4,Y ; bytes
STA $FFDF ; Make RAM appear at 0x8000+
STD ,Y++ ; Write
STX ,Y++ ; 6
STU ,Y++ ; bytes
CMPY #$FEFC ; While not at top of vector table
BLO copy6 ; ...keep looping (back to make ROM appear at 0x8000+)
copy2:
CMPY #$FF00 ; While not at #$FF00 (I/O space)
BHS done
STA $FFDE ; Make ROM appear at 0x8000+
LDD ,Y ; Read 2 bytes
STA $FFDF ; Make RAM appear at 0x8000+
STD ,Y++ ; Write 2 bytes
BRA copy2 ; Jump back to check for Y >= 0xFF00
done:
Notes: Here’s an example ROM to RAM copy routine. It starts by copying 6 bytes at-a-time, and then finalizes with a 2 byte at-a-time copy. You can see that it keeps switching the SAM back and forth between mapping upper memory to ROM (during reads) and RAM (during writes).

## Slide 13: CoCoVGA Enhanced Feature Access
6847 VDG has only 5 “mode” pins accessible via PIA – but it’s a DMA engine...
CoCoVGA uses these 5 mode pins (CSS, A/G, GM[2:0]) as combination lock during vertical blank
Tells CoCoVGA that next video frame is not video but is instead configuration data
During this time CoCoVGA displays previously buffered video data
Some shadow RAM regions for config data useful...
Notes: Here’s an overview of how we are going to access these enhanced features of CoCoVGA. I don’t have the code for this particular procedure in this slide deck, but suffice it to say it’s available on my web site should there be interest.
The important takeaway is that we not only need our machine language routines in this upper memory region we’re talking about, but we also need at least one shadow memory region that we can point the SAM to, allow the VDG to stream from, and enable CoCoVGA to consume as data, not video.

## Slide 14: Allocation of Upper RAM
Region | Size | Contents
$E000-$EBFF | 3072 | Optional CoCoVGA character set load region
$EC00-$EDFF | 512 | CoCoVGA page 0 register shadow load region
$EE00-$FEFF | 4352 | CoCoVGA BASIC tables, code, and data
Notes: So based on the information about the memory map and CoCoVGA’s needs, let’s slice up that hex E000 to hex FEFF region this way!

## Slide 15: Page 0 Shadow Register Region
Notes: Here is an excerpt from the 512-byte page 0 shadow register region I mentioned earlier. Because it will remain in memory, we can write to it and have this copy lying about maintaining our understanding of CoCoVGA enhanced mode state and updating it as needed to upload to CoCoVGA.

## Slide 16: VWIDTH Dynamic Patch Table
* Note that both patch lists below contain address + 2 bytes per entry
* Of the 2 bytes of data, one is the patch and the other location is reserved
* for populating the original values from the ROM so that we can undo the
* patch when switching back and forth between vwidths
* Color BASIC patch
numpokes EQU 32
cbpokestart
FDB 0xA376 // 'COLUMN MASK (TAB CONFIG)
FDB 0x3F
FDB 0xA37B // 'LINE WIDTH (TAB CONFIG)
FDB 0x40
FDB 0xA350 // 'SCROLL 64 CHARS-AT-A-TIME (SCROLLING)
FDB 0x40
FDB 0xA354 // 'START OF LAST LINE MSB (SCROLLING)
FDB 0x15
FDB 0xA355 // 'START OF LAST LINE LSB (SCROLLING)
FDB 0xC0
FDB 0xA347 // 'END OF SCREEN BUFFER (PUT CHAR ON SCREEN)
FDB 0x15
FDB 0xA8DE // 'TOP OF SCREEN (SET/RESET)
FDB 0x0E
...truncated for legibility...
Notes: Here’s another table which belongs in the hex EE00 to FEFF region. Those who remember my 2017 Tandy Assembly presentation of patching BASIC for the 64-column CoCoVGA text mode may recall that I had distilled down the patch to 32 bytes scattered around within Color BASIC and Extended Color BASIC to make it so SET/RESET, PRINT and PRINT @, cassette load status, and other sorts of things ended up in memory in the right place for 64-column mode. (If not, this presentation is published on the CoCoVGA web site.)
This table contains address/data pairs – actually address/data/data tuples! The address is the location in the ROM (now RAM) that needs to be updated. The first byte is the value needed for 64-column mode, and the second byte will be filled in during initialization so that we can return or UNPATCH to 32-column mode.

## Slide 17: Upper RAM Data/Variable Initialization
initccvbas ; Called first by ccvbasic.c to set known initial VDG/SAM
LDA #2 ; Assume BASIC is using page 2 (0x400 or 1024 dec) for now
STA videopage
CLRA ; Assume BASIC is using text mode TODO FIXME may not be true!
STA videomode
STA sammode
LDA #32 ; BASIC should be in 32-column text mode
STA curwidth
* Save ROM's copy for recovery from 64-column mode back to 32-column mode for vwidth
LDX #cbpokestart
LDB #numpokes
saveromloop
LDA [,X++] ; get value pointed to by address, increment X to point to data
STA ,X++ ; store value, increment X to point to next
DECB
BNE saveromloop
LDD #ccvregaddr
LSRA ; New CoCoVGA register page is at 0xEC00 (/512 = 118)
STA ccvregpage
CLR ccvpage ; Default CoCoVGA page to load is 512 byte page 0, other option is 3072 byte page $18
regwipeinit
* Wipe CoCoVGA reg page
LDX #ccvregaddr
regwipe
CLR ,X+
CMPX #ccvregaddrend
BNE regwipe
RTS
Notes: This routine is called by the C code loader.
It sets up some global variables regarding system state, copies the 32-column mode original values into the table we just described, and clears out the shadow register page.

## Slide 18: VRESET
Example routine which takes no arguments
* vreset - Reset CoCoVGA and global variables
vreset
JSR vwidth32 ; unapply vwidth 64 patch
JSR initccvbas
LDA #$FF
STA ccvregaddr
JSR pgmcocovga ; program CoCoVGA right now
CLR ccvregaddr
RTS
Notes: Here’s one of the routines which takes no arguments. You may recognize its label as being the first one on the jump table list.
Nothing exciting here, just setting things back to their default state of undoing any 64-column patch if present, wiping the shadow register page, writing a “reset-all” into byte 0 of the shadow register page and uploading that to CoCoVGA.

## Slide 19: VSCANLINES on
Example routine which takes one numeric argument
fcerr EQU 0xB44A
getbyteargb EQU 0xB70B ; Get byte argument into B reg
* vscanlines - Enable/disable scanline effect
vscanlines
BNE nofcerr6 ; Z flag set by BASIC interpreter if arguments present
JMP fcerr ; No arguments present – error! VSCANLINES needs one numeric argument
nofcerr6
* set/clear scanline enable
LDX #ccvregaddr
LDA 5,X
ANDA #$FB
STA 5,X
JSR getbyteargb ; Get next argument following VSCANLINES token
ANDB #$01
LSLB
LSLB
LDX #ccvregaddr
ORB 5,X
STB 5,X * set edit mask
LDA 1,X
ORA #$04
STA 1,X
JSR pgmcocovga ; program CoCoVGA right now
RTS
Notes: Here’s an example of a command that takes a single numeric argument. Note that the Z flag is set if there are arguments present after the command token. We use this to complain through BASIC if the argument is missing.
The get byte arg B function (from the “ROM”/now RAM) is used to consume a value which is masked to become zero or one, and bit shifted to the correct location of byte 5, bit 2 of the CoCoVGA register page before it’s uploaded.

## Slide 20: VPALETTE slot, red, green, blue, now
Example routine which takes multiple comma-separated numeric arguments
checkcommab EQU 0xB26D ; Consume comma
getnumber EQU 0xB70B ; Get numeric argument into B reg
* vpalette - Reconfigure CoCoVGA palette
vpalette
BNE nofcerr1 ; If no args, FC error
JMP fcerr
nofcerr1
* For now, just convert palslot to an SG palette entry memory location
JSR getbyteargb
LSLB ; x2 since 16 bits per palette slot
ADDB #32 ; offset by 32 since palette entries start at byte 32
STB palslot
JSR checkcommab ; consume comma character
JSR getnumber ; get numeric value
STB palred
JSR checkcommab ; consume comma character
JSR getnumber ; get numeric value
STB palgrn
JSR checkcommab ; consume comma character
JSR getnumber ; get numeric value
STB palblu
...truncated for legibility...
Notes: VPALETTE is the command which takes the most arguments. In this case, they are all comma-separated, so we want to call back into the BASIC parser to consume these as well as to parse the numerical values. This code segment is truncated just to show these parts of interest.
The first argument is consumed by get byte arg B, as with VSCANLINES, however, we are using two new “ROM” calls to find the comma (checkcommab) and the next numeric value (getnumber).

## Slide 21
DEMO
Notes: With that, I’m all done dwelling on code segments and tables – let’s see it in action!
A couple more slides – future direction and references...

## Slide 22: Future Exploration
Could this be done without 64k RAM in a CoCo 1 or 2?
  For this example, not currently, given the need to patch and unpatch BASIC for 64-column mode
  HOWEVER, other BASIC enhancements could, placing them in lower memory (remember to CLEAR) and updating the command interpreter hook table at $13E
Could this be put in a ROM/EPROM/EEPROM?
  Not in its current form, given the self-modifying nature of this example, but perhaps as part of cartridge ROM that could self-bootstrap into a 64k RAM system
  HOWEVER, other BASIC enhancements could – ADOS is a real life example of this

## Slide 23: Acknowledgements/Further Reading
Guidance from CoCo Discord users – info on where to start:
  William Astle - Extended BASIC Unravelled II - COMVEC
  Robert Murphey - Rainbow Magazine – Cooking with CoCo by Colin J. Stearman, September 1984
Pierre Sarrazin – CMOC newcmd.c
Color BASIC Unravelled II
Disk BASIC Unravelled II